## Slide 1: Computação Paralela Mest. Engenharia Computacional Mest. Int. Engenharia Computacional
Ano letivo 2022/2023
Rui Costa, Nuno Lau

## Slide 2: CUDA
Parallel general purpose computation model
Introduced by NVIDIA in 2006
Allows using the GPU for the execution of general purpose applications
Acknowledgement: This lecture is based on “CUDA C++ Programming Guide”, v11.6, NVIDIA and older versions

## Slide 3: CUDA

## Slide 4: CUDA

## Slide 5: CUDA – CPU and GPU Architecure

## Slide 6: CUDA Architecture

## Slide 7: CUDA Computing Applications

## Slide 8: CUDA Automatic Scalability

## Slide 9: CUDA Kernel, Grid, Block, Thread

## Slide 10: CUDA Grid of Threads

## Slide 11: CUDA memory

## Slide 12: CUDA memory

## Slide 13: CUDA memory

## Slide 14: CUDA Compute Capability
Compute Capability 1.x
Global memory (read and write)
  Slow and uncached
  Requires sequential and aligned 16 byte reads and writes to be fast
Texture memory (read only)
  Cache optimized for 2D spatial access pattern
Constant memory
  This is where constants and kernel arguments are stored
  Slow, but with small cache
Shared memory (16 kb per MP)
  Fast, but take care of bank conflicts
  Can be used to exchange data between threads in a block
Local memory (used for data that does not fit into registers)
  Slow and uncached
Registers
  Fastest, scope is thread local

## Slide 15: CUDA Compute Capability
Compute Capability 2.x
Global memory (read and write)
  Slow, but now with cache
Texture memory (read only)
  Cache optimized for 2D spatial access pattern
Constant memory
  Slow, but with cache (8 kb)
Shared memory
  Fast, but slightly different rules for bank conflicts now
Local memory
  Slow, but now with cache
Registers (32768 32-bit registers per MP)

## Slide 16: CUDA Compute Capability
Compute Capability 3.x
Global memory (read and write)
  Generally cached in L2, but not in L1
Constant memory
  Cache shared by all functional units
Shared memory
  32 banks with two addressing modes
Local memory
  Cached in L1
Compute Capability 5.x
Global memory
  Identical to cp 3.x
Shared memory
  32 banks organized such that successive 32-bit words map to successive banks
Compute Capability 6.x
Compute Capability 7.x
Compute Capability 8.x

## Slide 17: CUDA Heterogeneous Programming

## Slide 18: CUDA
Kernel invocation
kernel<<< Dg, Db, Ns, S >>>
  Dg is the grid dimension (dim3 type)
  Db is the block dimension (dim3 type)
  Ns is the number of shared memory bytes
  S is the stream

## Slide 19: CUDA
Block
  threadIdx.x, threadIdx.y, threadIdx.z
    Identify the thread in the block
  blockDim.x, blockDim.y, blockDim.z
  threadID = x+y*Dx+z*Dx*Dy
  Threads are executed in warps
    32 threads of the same block with consecutive ids
    Blocks should have more than 32 threads

## Slide 20: CUDA

## Slide 21: CUDA
Grid
  blockIdx.x, blockIdx.y, blockIdx.z
    Identify the block in the grid
  gridDim.x, gridDim.y, gridDim.z

## Slide 22: CUDA
__global__
  Used to define kernel functions
  Called by CPU; Run in GPU
__device__
  Used to define device functions
  Called by GPU; Run in GPU
__shared__
  Used to declare variables that reside in shared memory

## Slide 23: CUDA main()

## Slide 24: CUDA kernel